## Slide 1: Pre-certification testing why, when, where, & how
James Jarvis
APRS World, LLC
www.aprsworld.com

## Slide 2: Why?
“Certification Testing”
  NOT DESIGN TESTING!
  NOT PROTOTYPE TESTING!
  Is expensive
  Is not convenient
  Likely need to be restarted if changes are made
Design should be tested before certification testing is started.

## Slide 3: When
As soon as possible!
Test components
Test sub-systems
Test systems

## Slide 4: Where
Office
Shop
Highway
Field

## Slide 5: Where - Office: Design for test
Design turbine to IEC standards.
Model test setup to IEC standards where reasonable and feasible

## Slide 6: Where - Shop: Dynamometer
Pros
Cons
Availability
Controlled lab environment
Controlled RPMs, torque
Mechanical forces can be measured
Ideal for safety testing
Generator testing only, no airfoils
Capital $$$ intensive

## Slide 7: Dynamometers, Blade
Photo from Windward Engineering / Endurance
Photo from APRS World, LLC

## Slide 8: Dynamometers, Generator
Use the same test equipment for production testing
Photo from Windward Engineering / Endurance
Photo from Bergey Wind Power Company
Photo from APRS World, LLC

## Slide 9: Where - Highway: Truck Testing
Pros
Cons
Availability
High Speed Winds
Cheap
Small turbines only
Non-laminar flow
Vibrations
Influenced by natural wind
Trees, power lines, sonic booms

## Slide 10: Field Test Sites, Facilities
Put in appropriate places, not just convenient places
Have un-restricted access to test site
  Customers expect turbine to work and make them $$$. Do not expect them to be your test sites.
Have appropriate basic infrastructure
  Shelter
  Power
  Internet
  Site access
Build what you need to, but remember that infrastructure takes a lot of time and $$$

## Slide 11: Shelter
Environmental protection
  Humans
    Warm, dry, out of the wind, and comfortable
    Food prep
    Communications
  Equipment
    Specific to test
Mini shop
  Supplies for basic maintenance and repairs
  Basic tools
  Heavy tools & fixtures
Safety Equipment
  Hard hats, climbing harness, fire extinguisher, first aid kit

## Slide 12: Bad Places to Work
Fact: Plywood alone does not
make humans comfortable
… but having a piece of plywood over your head would be an improvement in some places

## Slide 13: Good places to work, NREL
Photo courtesy of Amy Bowen / NREL
Photo from APRS World, LLC

## Slide 14: IP Cameras
Mega-pixel IP Cameras EVERYWHERE
Record video or periodic stills
Synchronize time between data sources
Place a camera very close to
turbine for infrared
Illumination at night
Cheap @ < $400 per camera

## Slide 15: IP Camera Example
6:09PM
6:10PM

## Slide 16: IP Camera Example, Continued
What I found
@ 8:55PM

## Slide 17: Data
Look at it daily or more
  Catch problems early
  Integrate with your normal workflow
    Daily e-mail?
    iPod Touch before bed and first thing in the morning?
    Second monitor at your desk?
Historical trends
  Example: Decrease in RPM at given wind speed could indicate broken blade.

## Slide 18: Turbines and Towers and Electronics (oh my!)
Certification is on turbine AND tower AND electronics
Develop strategy for testing sub-systems independently of each other
  Dynamometer is great for testing generator and generator / inverter combination.
Test all of the pieces together!
  Electronics do REALLY effect mechanical bits
  Turbines can REALLY effect towers

## Slide 19: When ready for certification testing?
Design is stable and meets relevant IEC standards
Turbine can survive for period of time and wind greater than what is required for endurance testing
When an approximation of all safety tests have been passed

## Slide 20: Conclusions
Git ‘r done
  Certification testing is perfection
  Pre-certification testing making sure you are ready for perfection
Move fast, be agile
Test everything independently and together
Test early, test often
Test with more than one unit!

## Slide 21: Be realistic!
e-mail: jj@aprsworld.com
web: www.aprsworld.com

## Slide 22: Slides cut for lack of time…

## Slide 23: Field Test Sites, Personnel
Service test sites internally or with contracted personnel.
No tinkerers
Good communicators!

## Slide 24: Good places to work, APRS World

## Slide 25: Good places to work, Windward Engineering

## Slide 26: IP Camera, Infrared Example

## Slide 27: HD Video Cameras
Use to capture likely events
  Example: Grid fault simulation
Quantity of data is staggering
  10’s of gigabytes per hour
  Hard to share over internet
Trade-off in size versus frame rate
  Example: 120 FPS at WVGA, 30 FPS at 1080p
Hard to time synchronize automatically
Incredibly boring to watch
Cheap @ $300 per camera
(HD Hero 2)

## Slide 28: VOIP – Voice Over IP
Inexpensive way to have reliable voice communications
Improve safety with fixed phone
for 911 / emergency
Three connections
  Power
  Ethernet / Internet
  Normal telephone
Cheap @ < $0.02 per minute + $5 per month

## Slide 29: Instrumentation
Wind
  Anemometer, wind vane
Weather
  Temperature, relative humidity, barometric pressure
Turbine
  Voltage & Current to inverter / controller
  Voltage & Current to grid / batteries
  Advanced sensors
    Vibration, Acoustics, Temperature, Oil health, etc

## Slide 30: Meta-instrumentation
Load Health, Grid Tied
  Grid voltage
  Grid frequency
Load Health, Battery Charging
  Battery voltage / state of charge
  Dump load
    Current
    Duty cycle
Instrumentation health
  Bus voltages
  Computer connectivity, storage, etc

## Slide 31: Instrumentation Redundancy
Instrumentation problem or turbine problem?
Consider different types / manufacturers of the same sensors

## Slide 32: Sensor Quality
Quality of sensors driven by certainty of data required.
  Your engineers are your customers.
Example: Does it matter if ambient air temperature reads 12ºC when it is 11.1ºC?

## Slide 33: Data, processing
Automate! We use SQL.
SELECT
LEFT(packet_date,16) AS dateBin,
COUNT(packet_date) as n,
MIN(windSpeed0) AS ws0Min,
MAX(windSpeed0) ws0Max,
ROUND(AVG(windSpeed0),2) AS ws0Avg,
ROUND(STDDEV_POP(windSpeed0),2) AS ws0Stddev,
ROUND(MIN(vBattDisp*iBattDisp),2) AS pMin,
ROUND(MAX(vBattDisp*iBattDisp),2) AS pMax,
ROUND(AVG(vBattDisp*iBattDisp),2) AS pAvg,
ROUND(STDDEV_POP(vBattDisp*iBattDisp),2) AS pStddev
FROM
view_nvc9am_classic_monopole
WHERE
packet_date>='2012-03-15 00:00:00' AND packet_date<'2012-03-15 00:10:00'
GROUP BY
LEFT(packet_date,16);

## Slide 34: Data, processing, continued