## Slide 1: Micro Wind for Remote Sites
James Jarvis
APRS World, LLC
jj@aprsworld.com
+1-507-454-2727

## Slide 2: My Definitions
Micro Wind
1,000 watts or less nominal power output
Remote Sites
Inconvenient to access locations

## Slide 3: Keys to Success: Use Solar
Solar!
  Reliable
  Cheap
  Easy
Use wind when you can’t get enough solar

## Slide 4: Keys to Success: Quality
Buy darn good stuff
Purchase price is always going to be cheaper than service cost or downtime

## Slide 5: Keys to Success: Plan for Stuff to Break
Design with redundancy
  but not the same components that break the same!
Minimize single points of failure
Don’t go overboard!

## Slide 6: Keys to Success: Die Gracefully
When everything fails, don’t destroy the battery bank
Always incorporate low voltage disconnects
Keep LVD power consumption ≈ battery self discharge rate

## Slide 7: Keys to Success: Keep an eye on things
Monitor
  system
  environment
  but don’t go overboard
Maintain
  do preventative maintenance

## Slide 8: Keys to Success: Design for Installation & Maintenance
Minimize field time
Keep records
Bring the correct tools

## Slide 9: 10 Second Technical: Turbine Selection
Site wind speeds versus cut-out speeds
  be sure to look at all time periods, not just annual averages
Icing, salt water, extreme temperatures, etc
Keep active electronics out of the turbine!

## Slide 10: 10 Second Technical: Make Use of Excess Power
Indoor dump load and outdoor dump load
  Heat building when needed
  Satisfy redundant dump controller requirements
Intelligent load control
  turn on heaters, compress air, fill water tanks, upload data, etc
  add useful loads
    generator block & fuel
    battery bank

## Slide 11: Design for Transportation
Select economically transportable components
  Observe ATV, snow machine, helicopter, etc weight and size limits
  If at all possible, use your customer’s normal modes of site access.

## Slide 12: Work in the easiest place possible
Pre-build as much as you can in your shop
  sub assemblies, wire harnesses, anything that requires small parts
  select vendors that make easy to install products!
Re-package parts and assemblies so they are easiest to handle in the field
  packing peanuts or shredded paper at a wind site?
On-site time is the most expensive time

## Slide 13: This is no fun at 0°

## Slide 14: More Tower? More Power? More $$$?
Unique sites and unique considerations!
What is wind shear coefficient here?

## Slide 15: 10 Second Technical: Towers
Tower and foundation cost typically 2 to 10 times price of turbine
Install time typically 20 to 100 times the install time of the turbine
Consider mounting to existing towers or even roof mounting
Optimize your tower selection!

## Slide 16: 10 Second Technical: Foundations
Use what the site already has!
anchor to existing concrete slabs or rock
  acrylic adhesive is my favorite
Consolidate available site materials into ballast for ballasted tower
  rocks in a super sack
  but do some math first

## Slide 17: 10 Second Technical: Controller Interactions
Make sure multiple charge sources aren’t fighting
  don’t allow fossil fuel generator to trigger wind dump load
  don’t dump while equalizing

## Slide 18: 10 Second Technical: Low voltage disconnects: use them!
Use low voltage disconnects to prevent damage to your batteries in the event of power source failure
Some turbines require no standby power and can be used to bring up a discharged battery
Turbines with MPPT or other active controllers typically require battery power to operate and cannot charge a discharged battery.
  make provisions for some other source to be able to bootstrap things

## Slide 19: 10 Second Technical: Telemetry
Put remote monitoring provisions into your system
Basic state of health data as minimum
Consider “web” IP camera view of turbine and PV
  decent quality outdoor web cameras are now <$500

## Slide 20: IP Camera Example
6:09PM
6:10PM

## Slide 21: IP Camera Example, Continued
What I found

## Slide 22: Telemetry - Satellite
APRS World / SPOT Satellite Telemetry
  Globalstar network
  Low cost SPOT network
  <$400 hardware & <$100 year data
  6 hour highly compressed message with
    Wind speed / gust / average
    Turbine RPM / average RPM / current
    Temperature
    Dump Load kWh, duty cycle, battery temperature
    Battery Voltage

## Slide 23: Satellite Telemetry Data Website
Example of historical data:
Example of “live” data:

## Slide 24: MRO
Do regular scheduled maintenance
Consider pre-emptive replacement of batteries and micro turbines

## Slide 25: Conclusions
Use solar!
Use the best parts with best track record
Monitor and maintain system
Plan, plan, plan