## Slide 1: Low Cost, Low Temperature Lab Shop Testing
James Jarvis
APRS World, LLC
www.aprsworld.com

## Slide 2: Need
South Pole field trial of WT10 wind turbine for IRIS / PASSCAL
  -83°C to -12°C
  APRS World WT10 wind turbine
    bearings, seals & cables
  Web Camera
    operation
  Instrumentation
    operation and accuracy

## Slide 3: Traditional Approaches: Thermal Chamber
Pros
Fast
Accurate
Able to thermal shock DUT
Cons
Expensive
Fragile

## Slide 4: Traditional Approaches: Field Testing
Pros
Actual conditions
Cons
Unpredictable
Expensive
Slow

## Slide 5: Traditional Approaches: Immersion (dry ice / acetone)
Pros
Easy
Available
Right temperature: -78°C
Cons
Liquid
Solvent compatibility
Very fast – thermal shocks
"Aldolrxnpic" by Original uploader was E kwan at en.wikipedia - Originally from en.wikipedia; description page is/was here.. Licensed under Public Domain via Wikimedia Commons - http://commons.wikimedia.org/wiki/File:Aldolrxnpic.jpg#/media/File:Aldolrxnpic.jpg

## Slide 6: Idea: Ultra Freezer
Two common ranges:
  -40°C and -85°C
Expensive new ($20k)
Cheap and plentiful used ($1k)
120V @ 20A or 240V @ 15A – easy!

## Slide 7: Ultra Freezer Pitfalls
Often sold because they have problems
Compressors and refrigerant are expensive
Cascade system means that problem anywhere in system will require multiple compressors and refrigerant charges

## Slide 8: Getting Colder: Liquid CO2
Sublimination point: -78.5°C
Cheap:$0.08 per pound
Off the shelf controllers
Readily available

## Slide 9: APRS World’s freezers
Original -85°C worked for a few hours, then died
Only -40°C freezers available given time and price constraints

## Slide 10: APRS World’s Freezer Modifications
So-Low -40°C Freezer
Liquid CO2 for sub -40°C operation
RTD (PT100) instrumentation
5cm instrumentation port

## Slide 11: APRS World’s CO2 Controller Modifications
Replaced unusual fittings with NPT
Added solenoid indicator light
Removed dead backup battery
Designed and built missing CO2 discharge tube

## Slide 12: RTD Temperature Instrumentation: ThermokLogger-RTD
4 x PT100 or PT1000 RTD 4-wire inputs
2 x programmable solid state relay outputs
SD card logging
Real time clock
LCD display
Optional wireless modems
RS-232 port

## Slide 13: RTD Temperature Instrumentation: ThermokUSB-RTD2
2 x PT100 or PT1000 RTD 4-wire inputs
USB interface
Modbus or streaming ASCII
Small (4 x 4.5cm)
DIN rail mountable
Open Source
  hardware
  firmware
  software

## Slide 14: Bearing Friction Testing
12-volt cordless drill with drive adapter for WTAPRS
DC power / energy meter
Lower power to turn turbine at given RPM => less bearing losses

## Slide 15: Instrumentation Port
2” SCH 40 Stainless Pipe
SCH 80 polypropylene pipe cap when not in use
Also provides CO2 vent
Almost a disaster when installing
  MFG instructions wrong!

## Slide 16: Results: Test Setup
< $2000 able to obtain South Pole cold
Fast ramps down with CO2
Slow ramps with refrigeration
Stable
Good remote monitoring

## Slide 17: CO2 and Refrigeration Fast Ramp
Chart: 
DUT powered up
-60°C set point reached
End of brief test
°C
seconds

## Slide 18: Results: WT10 / WT14
Bearings
  Molykote 33 grease works great!
  Standard low drag seals are okay
  No short term ball clearance issues
Drop (output) cable “Carol Super Vu-Tron Supreme”
  not bendable at “winter” temperatures
  installable at “summer” temperatures
Blades (glass filled nylon)
  gets stiffer as it gets colder
  good!
  field tested in Antarctica

## Slide 19: Results: Pelican Cooler
2 watts waste heat keeps cooler interior 20°C above outdoor ambient
Not bad for $250 MSRP COTS!

## Slide 20: Results: IP Camera
Vivotek IP8364 rated to -20°C
Mechanical IR cut filter expected to be a problem
Polyurethane insulated ABS sleeve developed
Camera interior stays ~30°C above ambient

## Slide 21: Results: Pi Camera / Weather Station
IP Camera
Weather Station
Wireless or 802.15.4 POE
~1 watts
IP67 enclosure
Linux based
Open source
Wide DC input voltage

## Slide 22: Questions and Comments?
James Jarvis
  APRS World, LLC
  jj@aprsworld.com
  507.454.2727
Information on our products:
http://www.aprsworld.com/